## Slide 1: Droplet Injection Scheme Brainstorm
Ajay Manicka

## Slide 2: Quick Recap
Tackling the problem of routing using MAPF-LNS2
  Dynamic introduction of droplets
  Merging droplets together
  Increasing occlusion zones accordingly
Performance of algorithm dependent on scenario file (start and end locations of droplets)
  Dynamic introduction of droplets can exacerbate this issue
  Need to optimize droplet injection scheme.

## Slide 3: Purpose
Aside from the routing portion of the DNA assembly problem, we can optimize the droplet injection scheme to more efficiently place droplets on the grid for quicker routing
We want to devise a conceptual framework to optimally define dynamic injection, droplet entry locations, and droplet merge locations.
By judiciously choosing droplet starting and ending locations, we have more control over droplet routes while streamlining DNA storage gene assembly.

## Slide 4: Preliminary Ideas
Three ideas
  Scheme 1: Constant Injection Rate
  Scheme 2: Constant Capacity
  Scheme 3: Always Full
A combination of these ideas may be suitable.

## Slide 5: Constant Injection Rate
Let n be a percentage of the chip axis
  If n = 10, then this represents 10% of the length of an axis
Let r be the rate of injection (time units)
We inject 3 * (n% * length of grid) at a rate of r to the chip.
If we have a 1000 x 1000 grid, we inject 300 agents to the grid at once along the edge.
  The spacing between each droplets along the edge should be uniform to ensure the maximum distance between each droplet on the grid initially.

## Slide 6: Advantages and Disadvantages
Advantages
Allows us to easily program the write speed.
Enters the grid distanced from other droplets
Simple scheme
Disadvantages
Can cause congestion issues based on values of n and r
Not adaptive – will continue to inject more droplets even if congestion becomes large

## Slide 7: High-level details
Choose the three reservoirs (one from each edge) to pull from.
Calculate sum of Euclidian distances of each starting node to all potential mixing locations
Choose mixing location with smallest sum.
Route three agents using MAPF-LNS2 to this location
Do this for all droplet “thruples” before physically moving them.
Challenges:
Computationally expensive to calculate all Euclidian distances
Must keep track of the state of all mixing locations – space complexity.

## Slide 8: Constant Carrying Capacity
Instead of injecting droplets at the same time, we inject up until carrying capacity is met and inject as routes are completed.
We define n as the carrying capacity, and we define r as initial injection rate.
We inject droplets at a rate of r until we reach n. Then we add droplets to the system as former routes are completed.

## Slide 9: Advantages and Disadvantages
Advantages
Better at handling congestion than constant injection rate because we specify maximum possible number of agents.
More reliable as the system shouldn’t be overloaded at any point.
Space complexity more predictable.
Disadvantages
Harder to measure write speed because it is variable based on space availability.
Longer runtime as a consequence of better reliability.
Performance heavily dependent on choice of n.

## Slide 10: High-level details
Begin injecting droplets following the constant injection rate scheme.
Once carrying capacity is met, stop injection.
Adaptively inject more droplets as other droplets complete their routes.
Challenges:
Determining the sufficient carrying capacity at the specified grid size. I believe this would be a function of number of droplets and area of grid occluded.
May be overly constraining the memory of machine without much benefit.
Larger time and space complexity in exchange for reliability.

## Slide 11: Always Full Boundary
We inject droplets to the edge of the grid based on availability.
Suppose we have a 500x500 grid, and we want 10% of 3 edges full (50 agents per edge – 150 total).
We place these agents evenly across the boundary (i.e. [5,0], [15,0], …, [495,0])
Once a droplet leaves the start location and is “sufficient distance” away, we fill its starting location.

## Slide 12: Advantages and Disadvantages
Advantages
Constantly injecting droplets keeping the board busy.
More efficiently using grid’s available space.
Disadvantages
A lot of droplets will stall at starting point.
Needlessly increasing space complexity.
Not clear if this will improve runtime, may just increase congestion.

## Slide 13: Thoughts / Remarks
The initial placement and dynamic droplet insertion problem is nontrivial
  Droplets should be placed at the edge, and initially placed in an even distribution.
  An idealized system would fully implement a constant injection rate and handle congestion internally.
  Building an intelligent-adaptive model to recognize congestion and slow the injection rate may be a good solution to explore.
  Measuring congestion with respect to carrying capacity could be good here.